## Slide 1: Enhancing and Detecting CO2 Plumes in Satellite Images Using Computer Vision Denoising, Inpainting, and Ridge Tracing
Erik Koene, Gerrit Kuhlmann, Dominik Brunner
Empa, Dübendorf, Switzerland
24/11/2021

## Slide 2: Content
Background
Denoising
Inpainting
Ridge tracing
Discussion & summary
Simple examples followed by an application to satellite data

## Slide 3: Background
Copernicus Carbon Dioxide Monitoring (CO2M) satellite constellation
  To be launched in 2025
  22 km2 resolution
  Measures CO2 [ ppm] and NO2 [ molecules/cm2] images
Purpose of this study
  Evaluate potential of established computer-vision techniques on satellite images
  Focus on detecting plumes in future CO2M satellite images
Used input data:
  Synthetic data generated in SMARTCARB project [Kuhlmann et al., 2021]

## Slide 4: Denoising – example 1: hard thresholding
Denoising (suppress incoherent noise)
Domain transform
Mute values below threshold
Inverse transform

## Slide 5: Denoising – example 2: Wiener filtering
Domain transform
Multiply with expected S/N
Inverse transform
Denoising (suppress incoherent noise)

## Slide 6: Denoising – BM3D
Hard threshold
Wiener filtering
3D (e.g., Wavelet) transform followed by hard threshold
and inverse 3D transform
3D (e.g., Wavelet) transform followed by Wiener filtering
and inverse 3D transform
Original input
Initial denoising
Noisy input
Denoised result
Initial denoised estimate
Select similar looking patches
Aggregate patches
Aggregate patches
[Dabov et al. (2007)]

## Slide 7: BM3D applied to satellite data
BM3D applied to satellite data
Noise free CO2 image
Noisy XCO2 image ()
BM3D denoised
Power plants
Berlin
17% structural similarity; +6 dB PSNR
4% structural similarity

## Slide 8: BM3D applied to satellite data
BM3D applied to satellite data
Noise free CO2 image
Noisy XCO2 and NO2 images
BM3D denoised using both inputs
Power plants
Berlin
53% structural similarity; +12 dB PSNR
4% structural similarity

## Slide 9: Inpainting is like a jigsaw puzzle without pieces
We complete jigsaw puzzles by trying to match patches that fit well with the surrounding data.
We perform inpainting in a similar way, but teach a computer to generate the missing jigsaw pieces, such that:
1. The filled patches look structurally similar to rest of image
2. The filled patches connect well to the rest of the image
3. The filled images looks ‘plausible’

## Slide 10: Inpainting with a neural network
Neural network
Neural network
L1 difference
How fake does it look compared to the groundtruth?
How similar to the groundtruth?
Similarity
How (dis)similar are the generated patches to existing patches?
[Zeng et al. (2021)]

## Slide 11: Example application on satellite data
Wind field
Inpainted image
Ground truth
The inpainted images appear realistic, and correctly connect plumes that were disjoint by cloud cover
Note: at this stage, we do not recommend to use inpainted data for emissions estimations, just as a way to connect disjoint plume patches.
Image masked by cloud cover
(addition of wind field reduces average L1 error by 55%)

## Slide 12: Example application on satellite data
Image masked by cloud cover
Wind field
Inpainted image
Ground truth
The inpainted images appear realistic, and correctly connect plumes that were disjoint by cloud cover
Note: at this stage, we do not recommend to use inpainted data for emissions estimations, just as a way to connect disjoint plume patches.
(addition of wind field reduces average L1 error by 55%)

## Slide 13: Neurite detection
[Meijering et al. (2004)]
Varying background strengths (due to stitched microscope images), varying contrast, in presence of noise

## Slide 14: Plume detection
NO2 (BM3D denoised)
Meijering
  [Kuhlmann et al., 2019, 2021]
Too sensitive…

## Slide 15: Plume detection
NO2 (BM3D denoised)
Meijering
  [Kuhlmann et al., 2019, 2021]
Selecting plume bodies fixed
to large sources only

## Slide 16: Plume detection
NO2 (BM3D denoised)
  [Kuhlmann et al., 2019, 2021]
Plumes are detected about 10% longer without connecting to close-by plumes
Meijering
Selecting plume bodies fixed
to large sources only

## Slide 17: Discussion & Conclusion
The methods thus far were only applied or trained on SMARTCARB data, but as of yet untested on real satellite images
Meijering method not well-suited for broad point-sources (such as city of Berlin), and detection of the late tail of plumes is only of limited value as emissions are more dispersed at that stage
Many further uncertainties remain to not just detect but also quantify plume emissions
BM3D shows a great potential for improving image quality by considering joint XCO2 and NO2 images
Image inpainting can connect disjoint plume pixels due to cloud cover remarkably well. NB: we recommend to use this for small cloud clover fractions only, as the data quality will be bad for large cloud cover fractions.
Meijering method can detect narrow plume features for long distances

## Slide 18: References
Dabov, K., Foi, A., Katkovnik, V., & Egiazarian, K. (2007). Image denoising by sparse 3-D transform-domain collaborative filtering. IEEE Transactions on image processing, 16(8), 2080-2095.
Kuhlmann, G., Broquet, G., Marshall, J., Clément, V., Löscher, A., Meijer, Y., & Brunner, D. (2019). Detectability of CO2 emission plumes of cities and power plants with the Copernicus Anthropogenic CO2 Monitoring (CO2M) missions. Atmospheric Measurement Techniques, 6695-6719.
Kuhlmann, G., Henne, S., Meijer, Y. & Brunner, D. (2021) Quantifying CO2 Emissions of Power Plants With CO2 and NO2 Imaging Satellites. Front. Remote Sens. 2:689838. doi: 10.3389/frsen.2021.689838
Meijering, E., Jacob, M., Sarria, J. C., Steiner, P., Hirling, H., & Unser, M. (2004). Design and validation of a tool for neurite tracing and analysis in fluorescence microscopy images. Cytometry Part A: the journal of the International Society for Analytical Cytology, 58(2), 167-176.
Zeng, Y., Lin, Z., Lu, H., & Patel, V. M. (2021). CR-Fill: Generative Image Inpainting With Auxiliary Contextual Reconstruction. In Proceedings of the IEEE/CVF International Conference on Computer Vision (pp. 14164-14173).